## Slide 1
ONGOING INPUTS OF PERSISTENT ORGANIC POLLUTANTS TO THE ANACOSTIA RIVER
Study partners:
USFWS
USGS
UMCP
DOEE
Nathalie Lombard, Mandar Bokare, Varapapa Thodpanich, Sam Magee,
Upal Ghosh
Department of Chemical, Biochemical, and Environmental Engineering, UMBC
Presentation to the
Leadership Council for a Cleaner Anacostia River
September 13, 2018
10:00 am – noon

## Slide 2
ONGOING INPUTS OF POLLUTANTS
Tributary
inputs
Upstream inputs
Air-water exchange
Flux from sediment
Human exposure from water through food chain
Dissolved concentrations control exposure
Contributions to water from:
1) Bed sediments
2) Inputs from tributaries and outfalls
3) Air-water exchange
Ongoing inputs difficult to characterize
Using state of the art monitoring approaches to quantify loads
Complements RI with new data on loads
Coordinated with USGS effort to characterize stormflow inputs
Outflow
CSO

## Slide 3
Hydrophobic chemicals partition between water and solid phases
Concentration in polymer can be related to the concentration in water
Performance reference compounds used to correct for non-equilibrium
PASSIVE SAMPLING FOR MEASURING FREELY DISSOLVED CONCENTRATIONS
New approach: Integrative passive sampling

## Slide 4
Water sampler
Mussel
Air sampler
SAMPLING LOCATIONS

## Slide 5
PCBs in water
Deployment July-September 2016
Dissolved PCBs exceed 10-5 cancer risk at several tributaries and in Anacostia River
Dissolved PCBs in LBC higher than in Anacostia River
Provisional data subject to change

## Slide 6
PAHs in water
Deployment July-September 2016
Provisional data subject to change

## Slide 7
DDx in water
Deployment July-September 2016
Provisional data subject to change

## Slide 8
Chlordanes in water
Deployment July-September 2016
Provisional data subject to change

## Slide 9
PCBs in mussels compared to surface water
Chart: Concentration in mussel Cmussel predicted (ng/g lipid)
| 0.01 | 0.1 | 1 | 10 | 100 | 1000 | 10000
Cpred=10*Cobs | 0.1 | 1 | 10 | 100 | 1000 | 10000 | 100000
Cpred=2*Cobs | 0.02 | 0.2 | 2 | 20 | 200 | 2000 | 20000
Cpred= Cobs | 0.01 | 0.1 | 1 | 10 | 100 | 1000 | 10000
Cpred=0.5*Cobs | 0.005 | 0.05 | 0.5 | 5 | 50 | 500 | 5000
Cpred=0.1*Cobs | 0.001 | 0.01 | 0.1 | 1 | 10 | 100 | 1000
PCB | 1.5095 | 10.0985 | 65.2448 | 84.8958 | 18.0529 | 210.4261 | 209.8213 | 258.5211 | 235.1819 | 54.2279 | 201.6932 | 125.3789 | 11.594 | 113.2993 | 22.2581 | 2.7016 | 2.0362 | 89.5036 | 15.2897
PAH | 62.7949 | 41.3826 | 213.2433 | 85.3445 | 214.5106 | 91.1238 | 1442.9401 | 2286.4553 | 211.2506 | 2752.0189 | 1530.4384 | 823.759 | 412.214 | 134.7525 | 44.8248 | 856.4598
OCP | 86.0121 | 136.5913 | 7.9362 | 81.4229 | 188.9855 | 260.567 | 57.302 | 92.0056 | 64.874
PCB bioaccumulation in deployed mussels reflect differences in freely dissolved concentration in surface water

## Slide 10
Chart: PCBs in suspended sediments (μg/kg)
| NEB | NWB | WAB | HIR | LBC-1 | WC-37 | WC-29 | R4-30 | R6-32 | R6-31 | R7-28 | R3-51 | KL-26 | R3-28 | R3-53
Suspended Sediments at base flow | 99.0483 | 211.4575 | 99.4389 | 52.6504 | 262.9137 | 246.5228 | 129.7671 | 0.45144 | 994.7488 | 125.6864 | 80.263 | 115.387 | 252.981 | 132.1377 | 151.3955
Suspended Sediments at storm flow | 3.0679 | 1.138 | 7.3848 | 22.8084 | 49.7646
PCBs in suspended sediments
Stormflow sediments cleaner than most of the bed sediments in Anacostia River
Baseflow sediments have higher PCBs than Stormflow sediments
Provisional data subject to change
Anacostia River

## Slide 11
Chart: Freely-dissolved PCBs (ng/L)
| NEB | NWB | WAB | HIR | LBC-1 | Anacostia River
Concentration at base flow | 0.30189 | 0.49345 | 0.72178 | 0.29592 | 5.4801 | 1.59
Concentration at storm flow | 0.025442 | 0.012872 | 0.064199 | 0.34298 | 3.649
Freely dissolved PCBs during baseflow and stormflow
Dissolved PCBs generally much higher during baseflow compared to stormflow
Exceptions: HIR and LBC
Dissolved PCBs in LBC higher than in Anacostia River
Provisional data subject to change

## Slide 12
Measured total PCB loads for the Anacostia River
Net PCB volatilization out from water
Lower Beaverdam Creek contributes the highest total PCB load
PCB source from sediment hot-spots and sink into cleaner sediments
Provisional data subject to change

## Slide 13
Measured dissolved PCB loads for the Anacostia River
Sediment hotspots and Lower Beaverdam Creek contribute most of the dissolved PCBs
Provisional data subject to change

## Slide 14
Sediment-water flux of PCBs
Above 200 ng/g, sediments act as a source of PCBs to the water column
Below 200 ng/g, sediments act as sinks of PCBs
Provisional data subject to change

## Slide 15
Initial Conclusions
New data using latest technology for measuring low levels of pollutants in air and water
Main sources of dissolved PCBs in river:
  Lower Beaverdam Creek
  Sediment Hot-Spots
Water concentration exceedances for human cancer risk
High concentration in water causing net PCB volatilization from Anacostia River
Pollutant concentrations in mussel reflect concentrations in water
Storm sediments cleaner than river sediments
LBC
NEB
NWB
Provisional data subject to change
Questions?
Hot spot