## Slide 1: Firearms Examination Unit SAB Document Review
April 17, 2020

## Slide 2: INTRODUCTION
Table of Contents:
Documents Reviewed
SAB Reviewers
Recommendation Summary
Comments & Responses per Document
Questions

## Slide 3: INTRODUCTION
Documents Reviewed:
FEU 01 Examination and Test Fire of Firearms and Weapons
FEU 02 Examination of Ammunition and Ammunition Components
FEU 03 NIBIN Operational Procedure
FEU 04 Serial Number Restoration
FEU 05 Distance Determination and Gunshot Residue Testing
FEU 06 Writing and Distribution of Reports
FEU 07 Preparation and Storage of Reagents
FEU 08 Mideo Caseworks Procedure
FEU 09 Equipment and Calibration
FEU 10 Ammunition Reference Collection and Standards
FEU 11 Firearms Reference Collection
FEU 12 Evidence Handling and Case Distribution (no comments received)
FEU 13 Estimation of Uncertainty of Measurement
FEU Training Manual

## Slide 4: INTRODUCTION
Scientific Advisory Board Reviewers:
Ms. Danielle O’Neill
Dr. Lakeisha McClary
Mr. John Paul Jones II
Dr. Jeanne Jordan
Mr. Robert Thompson

## Slide 5: INTRODUCTION
Recommendations Summary
Recommendations Received: 141
Recommendations Accepted: 88
Questions Answered: 33
Recommendations Not Accepted: 18
*Requests for additional guidance: 2

## Slide 6: FEU 01: EXAMINATION OF FIREARMS
Reviewer | Comment | Applicable Section | FEU Response
Jones & McClary | Replace “adhered” with “adhered to” and “protocol” with “protocols” | 3.1 All Firearms Safety protocol shall be adhered in Appendix A when handling firearms. | Noted; this will be corrected.
Jones | How do you know if it has been sawed off - don’t really know ground truth? Is there a description for that somewhere or could you say "Appearance of Barrel Shortening"? | 7.4.2.11 Sawed off | We know this through training; we look for rough or uneven contouring and toolmarks and by comparison to known model barrel lengths.
Jones | Is there a description of what this "Mechanical Function Test entails" as it does not describe how one should test the trigger, cylinder, magazine, loading, or [shooting] functionality. IT does not state what is or is not to be conducted during this activity just that you are supposed to do something. | 7.5.1 A mechanical function test shall be conducted to determine if the firearm functions as designed by the manufacturer. If the firearm malfunctions, the reason will be documented in the technical notes. | This is also learned through training, and is dependent on the type and design of firearm; it would be impractical to describe in detail what this entails for every type of firearm we encounter.
Jones | Replace “will” with “shall” | 7.7.1 and 7.8.1 When the barrel or overall length of a firearm measurement is requested, measurement methods listed in FEU-13 Estimation of Uncertainty of Measurement will be used. | These two are synonymous and both accepted by ANAB; but we will ensure that the use is consistent throughout the document.

## Slide 7: FEU 01: EXAMINATION OF FIREARMS
Reviewer | Comment | Applicable Section | FEU Response
Jones | Do you want to change to "repeatability" to align with your FEU 13 7.2.1.2 statement that "Repeatability for this study is the ability of the same examiner to measure the same item on different days" | 7.9.3.7 Repeat the test at least three times to ensure reproducibility and document the range determined. | Noted; yes, we will change this for consistency.
Jones | You don’t describe what the drop test actually is. One can assume that you just drop it on the floor but some kind of description or parameters would be helpful. | 7.10 Drop Test | This will be corrected; per Thompson’s comment, we will reference to SAAMI standard for this procedure.
Jones | For your safety section, you could reference the current Draft OSAC Standard - I believe your are [consistent] with this but you should review prior to adding | 13 References | Noted; this will be added.
Jones | For your barrel [and] overall gun length measurements you could reference the latest Draft OSAC Standard - I believe you are [consistent] with these but you should review prior to adding | 13 References | Our procedures for barrel and overall length measurements are largely aligned with this guidance; additional guidance will be taken from this document when reviewing the FEU 13 Estimation of UoM.

## Slide 8: FEU 01: EXAMINATION OF FIREARMS
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace “previously submitted firearms are detected” with “the firearms have not been submitted before for testing”. | 7.1.6.1 Analysts shall screen all firearms during preliminary examinations to ensure that previously submitted firearms are detected. | We have had instances in which firearms have been submitted previously; this is something we want to detect and track, because it may not be possible to prevent it.
McClary | Include the location of the Test Fire Worksheet (e.g., LIMS, FEUXX). | 7.2.6 The documentation of the test firing shall be completed on the Test Fire Worksheet at the time of the examination. The Test Fire Worksheet must be printed and returned with the firearm for any firearms being submitted to CEU/ECB. | Noted; this will be added.
McClary | Might there be language added to convey instances when "may be" is "should be", e.g., "The client request will denote which modes." or "The modes are left to the discretion of the analyst." | 7.2.8 Firearms may be test fired utilizing all firing modes in which the firearm is capable of discharging. | Noted; this section will be moved to Examiner section and second suggested wording used.
McClary | Replace “Arrest paperwork must be provided if a Test Fire Certificate is generate.” with “Arrest paperwork is required in order to generate a Test Fire Certificate.” | 7.2.10 Arrest paperwork must be provided if a Test Fire Certificate is generated. | Noted; this will be corrected.

## Slide 9: FEU 01: EXAMINATION OF FIREARMS
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace “mechanical function test” with “function test”. | 7.5.1 A mechanical function test shall be conducted to determine if the firearm functions as designed by the manufacturer. | Noted; this will be corrected.
McClary | Replace “firearm or parts” with “firearm and/or parts”. From other FEU documents, it's possible that two reference numbers may be required in some cases | 7.5.2 The reference number of a firearm or parts of a firearm from the FEU Firearms Reference Collection (FRC) shall be recorded in the technical notes. | Noted; this will be corrected.
McClary | Replace “If a request is made to restore the firearm to firing condition, a request from the United States Attorney's Office is not required.” to “A request to restore the firearm to firing condition is required, from [the client?] or the United State's Attorney's Office.” | 7.5.2 If a request is made to restore the firearm to firing condition a request from the United States Attorney’s Office is not required. | Noted; this will be changed to “Restore the firearm to firing condition upon notification to the contributor (in the comm log).”
McClary | This could benefit from being broken into at least two sentences. After several passes, I have not been able to accurately visualize the process to offer suggested wording. Also, is it supposed to be perpendicular to the tangent line? | 7.8.2 Measure the overall length of a firearm from a line which is parallel to the axis of the bore from a perpendicular tangential line which touches the rearmost point of the butt-plate to the muzzle. | Noted; this will be corrected to mirror language from ASB 060, Standard for Barrel and Overall Length Measurements for Firearms.

## Slide 10: FEU 01: EXAMINATIONS OF FIREARMS
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace “Do not allow individuals not involved in the testing process in the intake area work space, tank room, or firing range.” with “Only individuals involved in the testing process are allowed in the intake area work space, tank room, or firing range.” | Appendix A 1.17 Do not allow individuals not involved in the testing process in the intake area work space, tank room, or firing range. | The Appendix is written in second person imperative verb tense, which should be maintained throughout.
Thompson | Add: If there is any question as to the condition of the firearm to be safely test fired, hold until an evaluation from an examiner. | 7.2.2 Evaluate that the firearm is safe to be test fired (e.g. free from cracked barrel or bore obstruction). Use a remote firing device if required. The safety of all FEU staff members comes first. | Noted; this will be added.
Thompson | Document the test fire record that a reference magazine was used to complete the test firing. | 7.2.5 If a magazine is not provided, a Firearms Reference Collection (FRC) magazine may be substituted if available. | Noted; this will be added.
Thompson | Replace “rate of fire” with “mode of fire”. | 7.3.2 Additional testing may be required to determine the rate of fire, e.g. full automatic fire or burst mode. | Noted; this will be corrected.
Thompson | This full section should be completed by an examiner due to the necessary expertise in classification and possible future expert testimony. | 7.4.3.1 Action field: record ghost guns by typing “Ghost gun” in this field | Technicians have sufficient expertise to identify un-serialized firearms and perform test fire functions; more detailed examinations may be done by examiners.

## Slide 11: FEU 01: EXAMINATION OF FIREARMS
Reviewer | Comment | Applicable Section | FEU Response
Thompson | Reorder to 7.5.2. This section may make more sense in the proposed change in order to after 7.5.1. | 7.5.4 If the firearm is received without a request in a condition further than a field strip, the FEU member will not reassemble the firearm and attempt to test fire without a letter from the U.S. Attorney’s Office on their letterhead. | Noted; this will be corrected.
Thompson | Replace “modifications” with “after-market modifications” | 7.5.3 Any modifications that are observed shall be documented on the firearms worksheet. | The more general term is preferred to encompass any type of modifications or customizations.
Thompson | Perhaps an introduction defining the scope of these; BB/Pellet air gun, blank gun, "Airsoft" (?), gas guns. Or are you only scoping BB/Pellet air guns ? | 7.6 Simulated/Improvised weapons | Definitions for these will be included in INFO 03 Definitions.
Thompson | Replace “double check” with “check” | 7.9.1 Double check and make sure that the firearm is unloaded. | Noted; this will be corrected.
Thompson | The drop test protocol should be referenced to a SAAMI standard at the end. If the SAAMI standard is adapted for DC lab use, then that should be references, also. | 7.10 Drop Test & 13 References | Noted; this will be added.

## Slide 12: FEU 02: EXAMINATION OF AMMUNITION
Reviewer | Comment | Applicable Section | FEU Response
O’Neill | Change “hollow point type projects” to “projectiles/ammunition” | 7.4.1 Petals from hollow-point type projects can be folded to expose land and groove impressions for microscopic and macroscopic examinations. | Noted; this will be corrected.
Jones | What are the criteria for identification? How do you determine an ID vs Elimination - is there a minimum number of corresponding features - if so what are they. | 7.7 Range of Microscopic Examination Conclusions | AFTE Theory of Identification is employed; there is no minimum number of corresponding features. This is detailed in the Training Manual.
Jones | Add statement describing how verifying examiner is selected - Example "FEU Manager [assigns] verifying examiner to perform the verification". [Trying] to address the possibility of having examiners always picking the same reviewer which could create potential bias. | 7.8 Verifications | Verifiers are chosen by the examiner based on availability and current workloads; there are limited options to choose from for verifying examiners. FEU Management monitors issues of potential bias in verifications and addresses on an as-needed basis.
McClary | Replace “LOM 1” with “LOM 01”. | 7.4.1.2 If the item is too small, label the container as per LOM 1. | Noted; this will be corrected.

## Slide 13: FEU 02: EXAMINATION OF AMMUNITION
Reviewer | Comment | Applicable Section | FEU Response
McClary | Should a photograph be taken prior to altering the projectile? | 7.4.1 Petals from hollow-point type projects can be folded to expose land and groove impressions for microscopic and macroscopic examinations. | Overall photos are already taken of each item; analysts may use discretion in when the photo is taken, and reviewers ensure that the photos taken are sufficient to support the notes.
McClary | Consider requiring that the bullet should be mounted to minimize errors that may arise from holding it. | 7.5.2 & 7.5.3 Hold or mount the fired bullet on a steady surface beneath the microscope… | Examiners are responsible for ensuring that their measurements are accurate, and may use discretion in the best way to measure the bullet.
McClary | Replace with “Perform three searches of the GRC file, one of search for each of the validation sets below.” | 7.6.3 Perform three searches of the GRC file, each with one of the below validation sets. | Noted; this will be corrected.
McClary | Replace “same firearm, or the submitted firearm” with “same firearm, and/or the submitted firearm”. | 7.7.1 Marks on the evidence ammunition components were produced from the same firearm, or from the submitted firearm. | Noted; this will be corrected.
McClary | Replace “Identification, Inconclusive, and Elimination” with “Identification, Elimination, and Inconclusive”; parallel to 7.7.1. | 7.8.1 In accordance with current FEU policy, 100% verification of microscopic conclusions of Identification, Inconclusive and Elimination shall be conducted… | Noted; this will be corrected.

## Slide 14: FEU 02: EXAMINATION OF AMMUNITION
Reviewer | Comment | Applicable Section | FEU Response
McClary | What is meant by "verification:? repeating tests, simply verifying that data make sense, checking the GRC verification log, or something else? | 7.8.3 Verification Documentation | Verification means independently repeating microscopic examination; other aspects of review are addressed in technical and administrative review.
McClary | Is there a process for documenting why certain tests were performed or not performed? | 11.1 Due to damage or other factors, some or all of the above examinations might not be possible. It is at the discretion of the firearms examiner as to what examinations are necessary and if they should be conducted. | Yes; the decision process regarding what tests were/were not performed is recorded in examiner’s technical notes.
Thompson | Replace “numerical weight” with “weight” | 7.3.1 The numerical weight of the bullets and fragments | This correction will be obsolete, as the requirement will be removed in updated version.
Thompson | Procedure for examinations should be prior to 7.7. "Range of Conclusions". Methodology that includes but not limited to; determination of toolmarks of value, observations using stereo and comparison scopes, documentation of magnification, manufacture marks both prior and after firing, firearm surface features that support identification, etc. Order of examinations; Q to Q, K to K, Q to K. | N/A | Noted; this will be addressed in a section added to the Training Manual to cover bias as it relates to process, scientific method, and the AFTE Theory of Identification.

## Slide 15: FEU 02: EXAMINATION OF AMMUNITION
Reviewer | Comment | Applicable Section | FEU Response
Thompson | The verifying examiner shall conduct an independent verification where the reporting examiner's results are not known and document the result of the verification, initial and date on the verification worksheet. | 7.8.3.2 The verifying examiner shall conduct an independent verification and document the result of the verification, initial and date on the verification worksheet. | Noted; this will be changed, with the following addition: The verifying examiner shall conduct an independent verification where the reporting examiner's results are not known prior to examination and document the result of the verification, initial and date on the verification worksheet.
Thompson | Replace “objective evidence” with “objective support” | 7.8.4.1 If the reporting and verifying examiner reach different results, they shall discuss and provide objective evidence of how the results were reached & 7.8.4.2.1 The FSL Quality Assurance specialist and FEU Management shall be notified in writing, and review the results and objective evidence provided by examiners | Noted; this will be corrected.

## Slide 16: FEU 03: NIBIN OPERATIONS
Reviewer | Comment | Applicable Section | FEU Response
Jones | What are the criteria for identification? How do you determine an ID vs Elimination - is there a minimum number of corresponding features - if so what are they. | 7.5.3 Identification | AFTE Theory of Identification is employed; there is no minimum number of corresponding features. This is detailed in the Training Manual.
Jones | Add statement describing how verifying examiner is selected - Example "FEU Manager [assigns] verifying examiner to perform the verification". [Trying] to address the possibility of having examiners always picking the same reviewer which could create potential bias. | 7.6 Microscopic Verifications | Verifiers are chosen by the examiner based on availability and current workloads; there are limited options to choose from for verifying examiners. FEU Management monitors issues of potential bias in verifications and addresses on an as-needed basis.
McClary | The indentation is shifted relative to the overall formatting. | 1.2, 2.2, 7.6.1 & 7.6.9 | Noted; this will be corrected.
McClary | Add space between cartridge and cases. | 2.1 …analysis of fired cartridgecases | Noted; this will be corrected.
McClary | Replace with “All three Regions of Interest (ROI) shall be acquired. Or All three Regions of Interest (ROI) shall be [acquired] by the System.” | 7.3.2 All three Regions of Interested (ROI) shall be acquired onto the System, if present on the fired cartridge cases. | Noted; this will be corrected.

## Slide 17: FEU 03: NIBIN OPERATIONS
Reviewer | Comment | Applicable Section | FEU Response
McClary | Switch (b) and (c ) to be consistent with FEU 02 order. | 7.5.3 Microscopic Examinations; Identification, Inconclusive, Elimination | Noted; this will be corrected.
Thompson | Require that the technician has noted and documented that the calibration and calibration results were completed correctly and the results were within requirements. | 6.1 An automatic calibration is performed of the NIBIN System after every 50 acquisitions. | Calibrations of the NIBIN hardware are the responsibility of FTI and ATF; this system is not maintained by the FEU, and therefore FEU does not retain its records. Calibration records may be located within the IBIS software if needed.

## Slide 18: FEU 04: SERIAL NUMBER RESTORATION
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace with “Ensure proper ventilation is available and employed.” | 3.6 Ensure proper ventilation is provided. | Noted; this will be corrected.
McClary | IUPAC nomenclature is the preferred to the historical naming of these compounds. | 4.2.5 Acidic Ferric Chloride 4.2.6 Ferric Chloride | Noted; this will be corrected.
McClary | The solution recipe for phosphoric acid and nitric acid solution is not in Appendix B. | 7.1.2 See Appendix B for solution recipes | Noted; this will be corrected.
McClary | Replace with “Case notes shall include the reagents used and verify that reagents were tested.” Are technical notes and case notes the same thing? The language suggests that it's [permissible] to not test the reagents, but this contradicts 7.4.1. | 7.4.6 Case notes shall include the reagents used and whether or not the reagents used were tested. | Noted; this will be corrected.
McClary & Jones | Be consistent with reporting milliliters. Ml, mL, space vs. no space; Is there a reason that iron(II) carbonate is underlined? | Appendix B Chemical reagents | Noted; this will be corrected.

## Slide 19: FEU 04: SERIAL NUMBER RESTORATION
Reviewer | Comment | Applicable Section | FEU Response
McClary | Where does the chloride come from to make iron(III) chloride? | Appendix B Chemical reagents | Noted; it should be listed as chloride, not carbonate; this will be corrected.
McClary | Specify that concentrated HCl is required, or provide the molar concentration to be used. | Appendix B Chemical reagents | Noted; this will be corrected.
McClary | Iron(III) chloride forms an acidic aqueous solution. Is the purpose of "acidic ferric chloride" to further decrease the pH? | Appendix B Chemical reagents | Yes; it is meant to provide an option for chemical etching that has a pH lower than ferric chloride.
Thompson | Add: Make sure all necessary firearm function and test fire examinations have been conducted prior to serial number restoration. | 7.2.1 Inventory evidence to be examined and mark the firearm in such a way as to allow for any future recognition or identification. | Noted; this will be added.

## Slide 20: FEU 05: DISTANCE DETERMINATION & GSR
Reviewer | Comment | Applicable Section | FEU Response
Jones | Does DFS have validation tests or literature to back up the claim that these swabs can be stored [indefinitely] and maintain their positive control status? Seems like there would need to be come controlled study to allow coated swabs to remain in use [indefinitely]. | 7.3.1.3 There is no known limit to the shelf life of these swabs. | These swabs are control tested with reagents prior to use in case work; however, these will follow the same procedures as chemical reagents (to be revised per O’Neill’s comment).
Jones | Add statement describing how verifying examiner is selected - Example "FEU Manager [assigns] verifying examiner to perform the verification". [Trying] to address the possibility of having examiners always picking the same reviewer which could create potential bias. | 7.10 Verification of Results | Verifiers are chosen by the examiner based on availability and current workloads; there are limited options to choose from for verifying examiners. FEU Management monitors issues of potential bias in verifications and addresses on an as-needed basis.
McClary | Replace “stereomacroscope” with “[stereo] microscope”. | 4.1 stereomacroscope | Noted; this will be corrected.
McClary | Is the desensitized photo paper purchased from a vendor or is it prepared in-house? If in-house, where might one find the instructions to do so? | 7.3.2.1 The desensitized photo paper mentioned below is simply photographic print paper which no longer bears light-sensitive silver salts in its surface emulsion. | Yes, it is purchased from a vendor, not prepared in-house.

## Slide 21: FEU 05: DISTANCE DETERMINATION & GSR
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace “preclude the potential spattering” with “avoid the potential spattering”. | 7.3.4.1 Gently pour the acid into the water to preclude the potential spattering of undiluted acid. | Noted; this will be corrected.
McClary | Some of the text is in a different font. Merge formatting. | 7.4.4 N/A | Noted; this is not present in the Qualtrax controlled document, but will be checked for formatting.
McClary | Is it appropriate or necessary to quantify what is meant by "small amount"? | 7.6.2.1 Place a small amount of sodium rhodizonate in a beaker and add sufficient distilled water until the solution turns the color of dark tea. | No; the GSR Manual (AFTE Journal: Dillon, Vol 22 No 3 1990, p251) states that a small amount should be used to create a “dark tea” consistency.
McClary | Replace “grains” with “grams”. | 7.6.3.1 120 grains & 7.6.3.2 90 grains | Noted; while solid reagents are generally weighed in grams, the GSR Manual provides instructions for weighing in grains for this procedure.
McClary | Add “and expiration date (one year from preparation date)”. | 7.6.3.8 & 7.6.4.6 Label the bottle with the name of the reagent, the date made (lot number MM/DD/YY) and preparer’s initials. | Noted; this will be added.
McClary | This step is separate here whereas just above in 7.6.3.8 it is included. Consider editing to make descriptions of similar preparations consistent with respect to formatting. | 7.6.4.7 Enter the appropriate information into the FEU chemical preparation log | Noted; this will be corrected.

## Slide 22: FEU 05: DISTANCE DETERMINATION & GSR
Reviewer | Comment | Applicable Section | FEU Response
McClary | Is there a protocol for if/when no pink color is observed? | 7.6.7.2 This solution shall eliminate the general yellow background color caused by the sodium rhodizonate and shall establish a local pH of 2.8, turning any lead, as well as other metals that may be present, a pink color. | No; if positive control works as expected, no additional test is needed to ensure reagents are working, regardless of whether a color change is noted during this step.
McClary | Replace “Indexing in pencil is preferable…” with “DO NOT USE INK at this point because it may bleed during the application of reagents (is it also true, as in 7.4.3 that the ink may transfer back to the tested item? If so, just cut and paste that sentence here)” | 7.7.2 Indexing in pencil is preferable since ink may bleed during the application of reagents. | Noted; this will be corrected.
McClary | Is there a way to set this test up so that a photograph can be quickly taken? If the color fades, then the pertinent visual evidence of a color change won't be visible on the filter paper. Can the filter paper be treated in such a way in the future to "force" another color change? Are there time limits or specific conditions for future visualization? | 7.7.6 & 7.7.7.4 Prompt note-taking is essential in that sometimes the color can fade rapidly and unpredictably. | Noted; will add a requirement to photograph any positive results.

## Slide 23: FEU 05: GSR & DISTANCE DETERMINATION
Reviewer | Comment | Applicable Section | FEU Response
McClary | How then does one determine a positive result? Is the Standard Transfer Method used often or is its use limited because of this limitation? | 7.7.7.3 Such transfers usually reflect positive results which are very vague and indistinct in form. | Yes, its use is limited; any color change is considered a positive result.
McClary | Replace with “Shooting events are dynamic and often complicated. Gunshot residue patterns…” | 11.4 Shooting events are dynamic and often complicated, gunshot residue patterns… | Noted; this will be corrected.
Thompson | Add list of validated inkjet photopaper that can replace "Desensitized Photographic Paper". | 7.3.2.1 The desensitized photo paper mentioned below is simply photographic print paper which no longer bears light-sensitive silver salts in its surface emulsion. | Noted; this will be added.
Thompson | Employing bracketed test fire distances and bracketed estimates of proximity should be described to answer measurement uncertainty. | 10.1 Uncertainty of Measurement not applicable | Uncertainty of Measurement is not applied to this test method because an estimation of UoM cannot be calculated with measurement results as range (ANAB Fundamentals of Measurement Uncertainty 2018). GSR/distance determination will be addressed as a limitation in FEU13 Estimation of Uncertainty of Measurement.

## Slide 24: FEU 06: REPORTING
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace with “Re-examination reports and supplements shall be…” to be parallel to 7.2. | 7.3.2 Supplements and re-examination reports shall be… | Noted; this will be corrected.
McClary | [D]remel polishing was not a test method included in FEU04. | 7.4.2.2 Serial Number Restoration – shall indicate test method as “dremel polishing”, “magnetic restoration” and/or “acid etching”, or other method to reveal the serial number. | Dremel polishing is a preparatory step prior to either magnetic or chemical restoration, but it may be the only step needed; it is not a separate test method.
Thompson | Replace “acid etching” with “chemical etching”. Not all the reagents are acid formulations. |  | Noted; this will be corrected.
McClary | Capitalize Griess in “modified Griess test”. | 7.4.2.3 Gunshot Residue – shall indicate test method as “modified griess test” and/or “sodium rhodizonate test” and/or “muzzle to garment distance determination”. | Noted; this will be corrected.
Thompson | Do not insert the questioned magazine if a determination is required to determine if the magazine was ever inserted in the suspect firearm. | 7.4.7 Indicate whether the magazine fits and functions in any of the submitted firearms. | Noted; an instruction will be added that if this examination is requested, no magazine will be inserted.
Thompson | For clarity, add what term(s) are proper, instead. | 7.4.8 The term “suspect bullet hole” is not to be used. | Noted; the term “defect” will be added.

## Slide 25: FEU 07: PREPARATION & STORAGE OF REAGENTS
Reviewer | Comment | Applicable Section | FEU Response
O’Neill | Add wording that reagents to be prepared in fume hood. | 3 Safety | Noted; this will be corrected.
O’Neill | Typical reagents is one year from opening then tested for continuous use if no expiration is listed. 5 years is a long time. | 7.3.1 Commercial reagents without a supplied expiration date will be given a date five (5) years from the date of receipt. | Request for clarification & guidance: What is common practice? What source may we reference for guidelines?
McClary | In other FEUs where chemicals are used, the clause "additionally the use of an N95 respirator mask is recommended" was not included. Is the mask recommended in the absence of a fume hood? In addition to the fume hood? | 3.2 …additionally the use of an N95 respirator mask is recommended. | The mask is recommended in addition to the fume hood; this will be corrected.
McClary | How often are the physical SDS updated? A time consistent with federal mandates (e.g., OSHA) should be included in 7.2.1 | 7.2.1 All reagents must have their SDS present in hard copy in the lab. Electronic copies should also be available and accessible in the network drive | SDS are updated when new reagents are purchased; this will be added.

## Slide 26: FEU 08: MIDEO CASEWORKS
Reviewer | Comment | Applicable Section | FEU Response
O’Neill | Not all worksheets are in Mideo; why not? Will they be? | 2.1 Not all worksheets are currently available in the System. | Photo-based worksheets are in Mideo, but request-based worksheets are still and will continue to be in LIMS (ex: TF, SNR, NIBIN, verification worksheets).
Jones | Fix footer macro | Footer | This is not present on controlled Qualtrax versions, and is related to removing them from the Qualtrax controlled document system.
McClary | Replace “was established” with “has been established”. | 2.1 As this new System is introduced in laboratory operations, a systematic approach was established to introduce authorized Mideo worksheets of the FEU. | Noted; this will be corrected.
McClary | Delete the semi-colon. | 2.2 …standard approach to complete worksheets and; comply with… | Noted; this will be corrected.
McClary | Replace with “Enter in the analysis date field the date the photos were uploaded.” Is there a place to include when the photos were taken? | 7.4.4 The date the photos were uploaded entered in the analysis date field | Noted; this will be corrected. In these worksheets there is no field for date that photos were taken.

## Slide 27: FEU 08: MIDEO CASEWORKS
Reviewer | Comment | Applicable Section | FEU Response
McClary | Is the deletion documented, if so where? Why might a PDF be deleted? Is that also included in the documentation (assuming the deletion is required to be documented). | 7.7.1 The PDF can be deleted and the data edited if necessary during the technical and administrative review. | The deletion is not required to be documented at this time, because the worksheet is considered a draft version of notes, such as the instance of a note-taking error made and caught in tech review.
McClary | Remove “may be” from “Images may be saved in Mideo Casework must be exported and saved in the LIMS Imaging Module.” | 7.9.1 Images may be saved in Mideo Casework must be exported and saved in the LIMS Imaging Module | Noted; this will be corrected.
McClary | The following required worksheets are not currently in Mideo Casework. They must be submitted [insert how/where e.g., in LIMS) | 12 Documentation | LIMS-generated worksheets are addressed in the relevant SOPs and LIMS guides, not in the Mideo SOP.

## Slide 28: FEU 09: EQUIPMENT & CALIBRATION
Reviewer | Comment | Applicable Section | FEU Response
McClary | Replace “encompass” with “encompasses”. | 1.2 Encompass a list of equipment requiring calibration… | Noted; this will be corrected.
McClary | Are these 3 different plans? | 7.1.3. All instrumentation and/or equipment shall have a calibration, performance checks and maintenance interval plan. | No; they are included in one plan; this will be re-worded for clarification.
McClary | Replace with “location in the laboratory. [Information] also indicates to which analyst the equipment is assigned.” | 7.2.2 …location in the laboratory, which shall indicate assignment to an analyst. | Equipment records indicate location of the item rather than specific analyst, because more than one analyst may utilize equipment at a given location.
McClary | What is meant by "these records"? The equipment inventory? | 7.2.4 Hard copies of these records are maintained in the laboratory in the Equipment Maintenance binder. | “These records” indicate the service and maintenance records, not the inventory; this will be re-worded for clarification.
McClary | Add “electronically, physically, or both”. | 7.3.13 The following equipment or instrumentation user manuals shall be readily available… | Noted; this will be corrected.
Jones | Fix footer macro | Footer | Previously addressed.

## Slide 29: FEU 09: EQUIPMENT & CALIBRATION
Reviewer | Comment | Applicable Section | FEU Response
Thompson | This balance described in the calibration protocol is relevant for weighing reagents and larger objects. Where is the calibration procedure for balances/scales that would be in the grain level for bullet weights? The use of 20g and 500g is not proper linear accuracy for smaller objects such as bullets. | 7.3.11.3 Performance checks- Balances | Noted; for now we will continue to use what we have, but we are purchasing a weight set in a more appropriate range.

## Slide 30: FEU 10: AMMUNITION COLLECTION
Reviewer | Comment | Applicable Section | FEU Response
McClary | Does the log include a place for the number of ammunition rounds removed, the number used in testing, and the number returned? | 7.1.1 & 7.1.2 Using ammunition from the Ammunition Reference Collection | No; ammunition inventory is kept by boxes, not cartridges. Due to volume, it would not be feasible to keep an inventory updated to specific numbers of cartridges used.
McClary | Replace “spread” with “spreadsheet”. | 7.6 The COOP Location Ammunition Collection Inventory referenced in the FEU Ammunition Inventory spread is located off site. | Noted; this will be corrected.
McClary | Is there a process to [acquire] desired ammunition? If so, where is that process located in the FEU or DFS documents? | 11.1 Not all ammunition encountered in case work may be found in the Ammunition Reference Collection and Standard Ammunition File. When desired ammunition is unavailable, analysts may use discretion in choosing “like ammunition” for examinations. | The process of acquiring ammunition is done during annual procurement orders, or as-needed; it is not documented in FEU SOPs because it is covered by DC government and agency purchasing protocol.
McClary | I didn't see FEU-LOG-02 in the documents. Does it exist? | 12.1 Documentation FEU-LOG-02 | Yes, it does. Only SOPs and Training Manual were requested for review, and not all controlled documents (including info sheets, forms, and logs) were sent.
Jones | Fix footer macro | Footer | Previously addressed.

## Slide 31: FEU 11: FIREARMS COLLECTION
Reviewer | Comment | Applicable Section | FEU Response
Thompson | Replace “waterproof” with “proof”. | 7.2.5 The location of manufacturing stamps, waterproof marks or serial numbers or numbering styles and formats. | Noted; this will be corrected.
McClary | The text is not aligned/is offset. | 7.3.1 & 7.3.2 Adding a firearm to the FRC | Noted; this will be corrected.
McClary | Archive firearm information from the database or spreadsheet. Is there a process for this? If so, where is it written? | 7.4.3 Archive firearm information from the database or spreadsheet | This process has not been previously specified because it has never happened and is not anticipated; guidance will be added that the information will be moved to another tab in spreadsheet in the event that the item is removed from the collection.
Jones | Fix footer macro | Footer | Previously addressed.

## Slide 32: FEU 13: ESTIMATION OF UNCERTAINTY OF MEASUREMENT
Reviewer | Comment | Applicable Section | FEU Response
Jones | Does this mean referencing section 7.2.1 that as long as the change in the total uncertainty is less than 10%, that then any specific changes in reproducibility, repeatability, and resolution of measuring equipment (no matter how large) will be considered "insignificant"? | 7.2.2 Changes to the contributing components listed in Section 7.2.1 that result in less than 10% of the total will be considered insignificant. | Yes; the estimations of UoM for these factors cannot be calculated individually in this study, so the significance of any changes must be determined by the change as a whole.
Jones | OSAC Firearms Draft standard for Uncertainty suggests 70 measurements minimum - you probably exceed this (See sections 4.5.5 - 4.5.7). | 7.2.1.2 & 7.3.3 Each examiner will take barrel and overall length measurements for each firearm every day for ten days. | Yes; this study included a total of 150 measurements.
Jones | What does this mean - not clear on what it applies too - if you buy more [than] 10 of these items or if the measurements of these individual items change by 10% each. | 7.6.2.1 The number items of equipment of a given type (ie: rulers, calipers) changes by more than 10% | It means if our total number of items (such as calipers) changes by more than 10%; e.g., if we have 10 calipers and buy 5 more, we have added 50% more items.
Jones | You could probably add a reference to ASB 060, Standard for Barrel and Overall Length Measurements for Firearms. | 13 References | Our procedures for barrel and overall length measurements are largely aligned with this guidance; additional guidance will be taken from this document when reviewing the FEU 13 Estimation of UoM.

## Slide 33: FEU 13: ESTIMATION OF UNCERTAINTY OF MEASUREMENT
Reviewer | Comment | Applicable Section | FEU Response
McClary | The SOP seems to have 2 purposes: (1) Complete a study to determine reproducibility, repeatability, and resolution of data using specific equipment and instruments in the laboratory and (2) to provide from that study measurements of uncertainty to be used by all FEU personnel. If my understanding is correct, then the scope of this FEU is imprecise. Only Section 9 details calculations and reporting. | 1.1 This Standard Operating Procedure (SOP) provides the steps required to calculate and report the estimation of expanded uncertainty of measurement for barrel and overall firearm length measurements. | The SOP does serve these two purposes; this will be updated for clarity.
McClary | The text is not aligned/is offset. | 7.6 Study review schedule | Noted; this will be corrected.
McClary | What are ranges of acceptable values for these uncertainty values? What is done if data from the study are outside the range(s)? | 9 Calculations | There are no known ranges of acceptable values for these uncertainty estimations; are there any sources available for this information?
McClary | Replace with “The free weight measuring equipment used is not calibrated and does not provide for more precise measurement increments than one quarter pound…” | 11.1 The free weight measuring equipment used is not calibrated and does provide for more precise measurement increments than one quarter pound… | Noted; this will be corrected.

## Slide 34: TRAINING MANUAL
Reviewer | Comment | Applicable Section | FEU Response
Jordan | Would it be possible to describe in more detail the interactions and responsibilities of both the trainer and the FSL training coordinator to the trainee? | P7 Roles and Responsibilities | Training division will be coordinating response.
Jordan | Point 4 about ethics and professionalism. How is this training carried out? | P9 The trainee should have an understanding of the ethical and professional responsibilities for FEU examiners to include | Training division will be coordinating response.
Jordan | Point 1; How is this information shared with the trainee? | P10 The FEU Trainee should automatically receive information pertaining to Objective 1 as a new employee. | All modules are reviewed with each trainee when assigned and prior to being signed off for completion. Mod 1 emphasizes more on orientation and in-depth one on one conversations with each trainee, which include tours.
Jordan | Should there not be a link to these DC firearm laws for the trainee to access? | P13 Know the firearms laws that govern the District of Columbia and the appropriate Federal firearms laws routinely used in this unit | This item will be removed.
Jordan | To be consistent, put a space between Points 6 and 7. | P14 (formatting) | Noted; this will be corrected.
Jordan | Will the trainee know the meanings of the abbreviations used here? GSR, NIBIN, etc. | P14 Describe the proper PPE worn while working in the following sections of the FEU. | Yes; these abbreviations are included in the abbreviations info sheet for the unit.

## Slide 35: TRAINING MANUAL
Reviewer | Comment | Applicable Section | FEU Response
Jordan | Periods are missing from Objectives. | P39, 67, 72, 95, 102 (formatting) | Noted; this will be corrected.
Jordan | Provide details to the trainee around what the length of the presentation should be. | P41-42, 49-50 Oral board; oral presentation and/or Powerpoint presentation | Length of presentations are dictated by the required content stated in “Module Objectives”, and will vary per module.
Jordan | Remove line space between Points 15 and 16. | P47 (formatting) | Noted; this will be corrected.
Jordan | Provide the trainee with the minimum number of these weapons that you expect them to disassembled and reassembled. | P49 Partially disassemble and reassemble the weapons listed above… | Trainee is required to “Partially disassemble and reassemble the weapons listed above, or designated by the Trainer, and prepare a FEU Firearm Worksheet for each.
Jordan | There are inconsistencies in the font type being used on text in these pages. | P55, P70, P77, P79, P86, P90, P95, P97, 103, 104 (formatting) | Noted; this will be corrected.
Jordan | Study Question 10: Will the trainee know what CMS stands for? | P60 Explain CMS. | Yes, Consecutive Matching Stria; will consider updating to: Quantitative Consecutive Matching Stria (QCMS) Biasotti, A. and Murdock, J.
Jordan | Use capital lettering for items in Point 15. | P61 (formatting) | Noted; this will be corrected.
Jordan | Practical Exercises/Skills; Point 1: Will the trainee be told what a passing grade is here (X/20 correct)? | P69 Your trainer will provide you with 20 different types of bullets… | The quantity of bullets (20) will be removed to alleviate confusion; the practical exercise does not contain a passing grade.

## Slide 36: TRAINING MANUAL
Reviewer | Comment | Applicable Section | FEU Response
Jordan | Point 12: Correct hydrochloric acid to be HCl. | P91 Hcl | Noted; this will be corrected.
Jordan | Point 5; Change to “Support your results with photographs.” | P98 Support your results by photographs. | Noted; this will be corrected.
Jordan | Provide definition for NIBIN. | P107 Efficiently, classify and sort cartridges cases by class characteristics for entry into the NIBIN system while maintaining the integrity of the evidence. | This abbreviation is included in the abbreviations info sheet for the unit.
Jordan | The figure legend is missing. | P112 (diagrams) | Noted; this will be corrected; remove P112 from Training Manual (P70 of 112: #3 remove Appendix Ref.)
Jones | Provide a reference and link to the Firearms Consensus Body at the AAFS Academy Standards Board (ASB). Provide a link to the OSAC Firearms and Toolmarks Subcommittee website which displays all the "OSAC Proposed" standards that have been introduced to ASB for formal [development] - this is where the leading practitioners are trying to move the discipline | N/A | AAFS ASB Firearms Consensus Body does not currently have any published documents on the site to reference; we will, however, stay updated on any guidance the group provides. OSAC reference will be provided to trainees.

## Slide 37: TRAINING MANUAL
Reviewer | Comment | Applicable Section | FEU Response
Thompson | Consider adding a module where all of the subspecialties are brought together in case examination approaches. EXAMPLES 1) When you have multiple bullets/cases what may be the best approach in the examination PROCESS so that the maximum relevant information can be determined. 2) In a GSR examination, what is the best PROCESS for the examination of a GSR pattern, fired bullets/cases, and suspect firearm, so that the best evidence results can be produced. | N/A | Noted; these examination processes are discussed in each relevant training module rather than a consolidated separate module. This will also be addressed in a section added to the Training Manual to cover bias as it relates to process, scientific method, and the AFTE Theory of Identification.

## Slide 38: TRAINING MANUAL
Reviewer | Comment | Applicable Section | FEU Response
Jordan | Include links to these websites referenced here in Point 1 under study/discussion questions for the trainees. | P19 Explain when an examiner should use the (AFTE) website and SWGGUN Admissibility Resource Kit website | Link is present in line 1 of recommended reading material.
Jordan | Periods are missing from the end of sentences in sections a), b) and c). | P24 (formatting) | Noted; this will be corrected.
Jordan | In all examples of Study/Discussion Questions, is the trainee required to submit their written answers to these queries? How do they demonstrate their competencies? | N/A | All trainees are required to submit written responses to all S/D Questions to the trainer who reviews for accuracy. Additionally, upon completion, group or one on one Q&A training sessions are held for review and to gauge trainee competency.
Jordan | Point 3; what criteria is used in determining successful completion of their oral boards? | P31 Successful completion of the Oral Board. | Oral Board panels are comprised of a three (3) SME who determine competency based on the following criteria: satisfies all objectives set forth in “Module Objectives”; presentation content and delivery; responses provided during Q&A session.
Jordan | In these evaluations; if the trainer is the only evaluator, does the trainee have the ability to ask for a second opinion if they believe they were successful? | N/A | Previously addressed- see above.

## Slide 39: QUESTIONS
FEU would like to thank the esteemed members
of the Scientific Advisory Board for their input and guidance.