## Slide 1: Tumor Prevalence in Brown Bullhead in the Anacostia River and Tidal Potomac Watershed: 1992-2016
Fred Pinkney
U.S. Fish and Wildlife Service
Chesapeake Bay Field Office
Annapolis, MD
Presentation to:
Leadership Council for a Cleaner Anacostia River
June 14, 2018

## Slide 2
John Harshbarger,
George Washington University
Medical Center
Mike Rutter, Penn State - Erie
Peter
Sakaris,
Georgia
Gwinett
College
COAUTHORS
FUNDING: DC DEPT ENERGY & ENVIRONMENT

## Slide 4: Acknowledgments
Department of Energy & Environment: Dev Murali, Bryan King, Danny Ryan, Eric Thadey, Luke Lyon, and Joe Swann.
USFWS: Steve Minkinnen, Josh Newhard, Mike Mangold, John Gill, Ian Park, and Rachel Harrison.
Funding: DOEE

## Slide 5: Background
Cancer-causing chemicals enter rivers, estuaries, and coastal waters and build up in sediments
Some bottom-dwelling fish species develop tumors
Tumor surveys have been used as an indicator of habitat quality and track cleanups: Puget Sound, Great Lakes, Chesapeake Bay

## Slide 6
Cholangiocarcinoma
Hepatocellular carcinoma
Liver tumors

## Slide 7
Skin lesions diagnosed as squamous cell
carcinomas,

## Slide 8
Brown bullhead: ideal species
Bottom feeder
  Small home range (2 km in Anacostia)
  Great Lakes and Chesapeake Bay tribs up to 8 ppt

## Slide 9: Polynuclear Aromatic Hydrocarbons (PAHs)
Over 100 chemicals
Found in fossil fuels-coal, gas, oil—tar, asphalt, pitch; runoff from roads, car exhaust, leaking oil
Accumulate in sediments
Some compounds cause cancer in humans, rats, mice, fish

## Slide 10: Relationship of biomarkers of PAH exposure
Benzo(a)pyrene
CYP1A as EROD
Diol epoxide
DNA adducts
Mutations
Oncogene activation
Tumor formation
Repair
Bile metabolites

## Slide 11
Standard DRZ typical
of PAC exposure
Radioactive zone
from additional
class of
compounds
Anacostia River
Tuckahoe River
Chromatograms of DNA adducts in brown bullhead livers from Anacostia and Tuckahoe Rivers and schematic. (DRZ= diagonal radioactive zone, PAC= polycyclic aromatic compound).
Schematic

## Slide 12
Polychlorinated biphenyls (PCBs): Banned (1979) but still in use
PCB Transformer contains concentrations greater than 500 parts per million (ppm)
PCB-Contaminated Transformers containing between 50 and 499 ppm
Other sources: capacitors, light ballasts, caulks, floor coatings, pigments

## Slide 13
PAHs
DNA adducts
PCBs,
DDT
LIVER CARCINOGENESIS IN FISH

## Slide 14
Spatial and temporal analysis
use the 25-year database to identify reference locations; test effects of age, length, sex, and weight
examine links with exposure to PAHs, polychlorinated biphenyls (PCBs), and DDT
OBJECTIVES: 2014-16 Study

## Slide 15
~ 50 brown bullhead > 250 mm per collection
Lab necropsy, aging, pathology
Logistic regression analysis
Sediment chemistry: 2015: 5 samples per location and compare with 2000 data
Interpret fish biomarker and tissue data
Methods

## Slide 18
USFWS sediment sampling locations at Bladensburg (ANABL; left) and near the CSX Bridge (ANAC; right).

## Slide 19
Potomac River showing the USFWS sediment sampling locations at Dyke Marsh (DYKE; left) and Piscataway Creek (PISC; right).

## Slide 20
Chart: Length (mm)
| 250 | 260 | 270 | 280 | 290 | 300 | 310 | 320
Anacostia O St.('01) | 0.78715 | 0.81742 | 0.84424 | 0.86776 | 0.8882 | 0.90582 | 0.92091 | 0.93376
Anacostia Upper ('00,'01) | 0.67523 | 0.71567 | 0.75292 | 0.78674 | 0.81706 | 0.84392 | 0.86748 | 0.88796
Anacostia CSX ('96,'01) | 0.63398 | 0.6771 | 0.71741 | 0.75451 | 0.78817 | 0.81834 | 0.84505 | 0.86846
Potomac-Roosevelt Is.('09) | 0.30365 | 0.34551 | 0.38992 | 0.43622 | 0.48367 | 0.53141 | 0.57859 | 0.62437
Anacostia CSX ('09-'11) | 0.2695 | 0.30874 | 0.35095 | 0.39563 | 0.44212 | 0.48965 | 0.53737 | 0.58442
Piscataway ('11) | 0.21159 | 0.24523 | 0.2823 | 0.32259 | 0.36569 | 0.41106 | 0.45799 | 0.50568
Anacostia CSX ('14-'16) | 0.10242 | 0.12138 | 0.14329 | 0.16839 | 0.19687 | 0.22886 | 0.26432 | 0.30312
Piscataway ('14-'16) | 0.1294 | 0.1525 | 0.17888 | 0.2087 | 0.24202 | 0.27879 | 0.31879 | 0.36166
Anacostia Bladensburg ('14-'16) | 0.072013 | 0.085879 | 0.10212 | 0.12103 | 0.14288 | 0.16793 | 0.19636 | 0.22828
Ches Bay Ref Group | 0.049794 | 0.059658 | 0.071328 | 0.085075 | 0.10118 | 0.11994 | 0.14163 | 0.1665
LIVER TUMOR PROBABILITIES: FEMALES

## Slide 21
Chart: Liver Tumors in 280 mm Brown Bullhead from Anacostia CSX Bridge area
| 1996, 2001 merged | 2009-2011 | 2014-2016 | Chesapeake Bay Reference Group | 1996, 2001 merged | 2009-2011 | 2014-2016 | Chesapeake Bay Reference Group
 | 77.8 | 42.5 | 18 | 9.4 | 48.6 | 16.6 | 5.7 | 2.7

## Slide 22
Chart: Length (mm)
| 250 | 260 | 270 | 280 | 290 | 300 | 310 | 320
Anacostia O St.('01) | 0.10038 | 0.12675 | 0.15882 | 0.19718 | 0.24213 | 0.29359 | 0.35091 | 0.41289
Anacostia Upper ('00,'01) | 0.10424 | 0.13147 | 0.16451 | 0.20391 | 0.24992 | 0.30237 | 0.36054 | 0.42311
Anacostia CSX ('96,'01) | 0.13067 | 0.16355 | 0.20278 | 0.24861 | 0.3009 | 0.35893 | 0.4214 | 0.4865
Potomac-Roosevelt Is.('09) | 0.048798 | 0.06256 | 0.079876 | 0.10147 | 0.12808 | 0.16043 | 0.19908 | 0.24434
Anacostia CSX ('09-'11) | 0.072559 | 0.092371 | 0.11691 | 0.14691 | 0.18302 | 0.22565 | 0.27487 | 0.33026
Piscataway ('11) | 0.037942 | 0.048798 | 0.06256 | 0.079876 | 0.10147 | 0.12808 | 0.16043 | 0.19908
Anacostia CSX ('14-'16) | 0.018505 | 0.023939 | 0.030917 | 0.039848 | 0.051221 | 0.065618 | 0.083706 | 0.10621
Piscataway ('14-'16) | 0.026364 | 0.034025 | 0.043813 | 0.056251 | 0.071956 | 0.091619 | 0.11598 | 0.14579
Anacostia Bladensburg ('14-'16) | 0.02282 | 0.029483 | 0.038015 | 0.048891 | 0.062677 | 0.080023 | 0.10165 | 0.1283
Ches Bay Ref Group | 0.015859 | 0.020532 | 0.026545 | 0.034256 | 0.044107 | 0.056624 | 0.072424 | 0.092203
SKIN TUMOR PROBABILITIES: FEMALES

## Slide 23
Chart: Skin Tumors in Female 280 mm Brown Bullhead from Anacostia CSX Bridge area
| 1996, 2001 merged | 2009-2011 | 2014-2016 | Chesapeake Bay Reference Group
 | 28.3 | 16.9 | 4.7 | 4.1

## Slide 24
 | ANABL |  |  | ANAC |  | 
 | ANS (n=4) | USFWS (n=4) | Statistics | ANS (n=19) | USFWS (n=5) | Statistics
Date | 9/20/2000 | 9/8/2015 |  | 9/20/2000 | 9/8/2015 | 
Total PCBs (ppb) | 99.3±19.0 | 20.7±7.8 | t-test, p<0.001 | 175±79 | 177±47 | t-test, p=0.96
Total chlordane (ppb) | 45.5±9.9 | 55.5±16.1 | t-test, p=0.33 | 54.6 (16.5, 147) | 57.5 (46.4, 60.5) | Mann-Whitney, p=0.91
Total DDT (ppb) | 32.1±11.8 | 17.0±3.8 | t-test, p=0.051 | 59.7±29.5 | 30.7±5.2 | t-test, p=0.02c
Total PAHs (ppm) | 32.2±11.3 | 25.8±10.0 | t-test, p=0.42 | 32.0 (18.3, 108) | 30.5 (27.3, 31.7) | Mann-Whitney, p=0.57
Carc PAH (ppm) | 13.9±4.4 | 7.94±3.12 | t-test, p=0.07 | 12.3 (6.0, 33.8) | 8.85 (8.37, 9.71) | Mann Whitney, p=0.09
Anacostia Sediments: 2000 vs. 2015

## Slide 25
Chart: Liver Tumors (%) vs. Total PAHs
| 22.403793999999998 | 30.011900000000004 | 6.8823075000000005 | 4.5916759999999996 | 1.4241118000000001 | 12 | 10.5 | 14.9 | 4.8 | 5.0999999999999996 | 26.8 | 30.9 | 28.1 | 15.2 | 6.8 | 0.2 | 1.8 | 6.5 | 3.4 | 1.5 | 4.5
Liver % | 12 | 17 | 4 | 17 | 3 | 7 | 7 | 17 | 17 | 7 | 55 | 68 | 60 | 53.5 | 0 | 3 | 10 | 8 | 20 | 0 | 3
Sediment total PAH (ppm)

## Slide 26: Why are liver tumors decreasing in the Anacostia bullheads?
PAH exposure
Sediment PAHs from collection areas: 2000 vs. 2015, maybe decreasing, few samples
Fish data: 2-4 fold decrease in PAC-DNA adducts 2000 vs. 2009—small sample size
PCB, DDT exposure
Sediment not consistent decrease: 2000 vs. 2015
Fish tissue data: strong decreases-~6-8 fold

## Slide 27
Chart: PCBs in Anacostia Brown Bullhead near CSX Bridge
 | 302 | 329 | 467 | 56

## Slide 28
Chart: Channel Catfish: Total PCBs and Total DDT in DC Waters (ppm wet weight)
| 2000 | 2007 | 2013
tPCB | 1.41 | 0.81 | 0.2
tDDT | 0.135 | 0.226 | 0.08

## Slide 29: Conclusions
Liver tumors down 4 to 8 fold since 2001in Anacostia bullheads from CSX Bridge area
Skin tumors down 6 to 7 fold in Anacostia bullheads
Anacostia CSX: still 2X background for liver; skin now similar to background
2014-16: Piscataway Creek=Anacostia but Dyke Marsh = background

## Slide 30: Recommendations
Monitor tumors on a 5-year cycle to track trends in DC and nearby locations
Use fish tissue and biomarkers to evaluate changes in exposure to liver carcinogens
Why is the skin tumor prevalence dramatically decreasing in Anacostia bullheads?
  Research to see if viruses may play a role

## Slide 31: YEAR OF THE ANACOSTIA
Tumors in fish: way down
Fish tissue contaminants: down
People enjoying the river: way up

## Slide 32
fred_pinkney@fws.gov